## Slide 1: Lab Zero: A First Experiment using GENI and FIRE
Sarah Edwards, GENI Project Office

## Slide 2: Hands On Exercise
Do a Simple Experiment
Reserve two VMs connected at Layer 2
Layer 2
VM
VM
Notes: There are three goals for today ….
First, jump right in and use GENI to do a very simple (layer 2) experiment

## Slide 3: Experiment Workflow
Part I: Design/Setup
Part II: Execute
Part III: Finish
Notes: We’ve split the experiment into several parts. Before each of these sections, we’ll talk about the concepts and terms you will need for each section.
The logo on the left is intended to act as a guidepost to help you keep track of where you are.

## Slide 4: Jacks and jFed are …
Graphical user interfaces (GUIs) for:
  designing topologies in GENI
  reserving resources in GENI
Notes: Jacks is a tool that is integrated into the portal which provides a graphical user interface for designing and reserving topologies in GENI.

## Slide 5: Experiment Workflow
Part I: Design/Setup
Part II: Execute
Part III: Finish
Notes: Now we’re ready for part I. We will start by making sure we have the right access to GENI resources. This is mostly ** one-time setup **.

## Slide 6: Part I: Establish Management Environment
1 Pre-work: Design your experiment
2.1 Pre-work: Create a GENI account
2.2 Pre-work: Project lead (aka professor) adds you to project
  Project Name: FGRE15 in GENI FGRE summit in FIRE
2.3 Generate and Download SSH Keypair
Notes: First, if you haven’t already, we’ll log into the GENI Portal.
Second, the project lead should have already added you to a project.
Third, we will generate and download an SSH keypair.

## Slide 7
You are here
Projects
Slices
Log Messages
Help
Profile
Tools
Map
Notes: If you haven’t already, login to the GENI Portal at https://portal.geni.net.
The Home page looks like this.
Going from top to bottom on the left, it lists all of the projects you are a member of and the slices you have. As well as a log of recent notable actions at the bottom.
The Home page has most of the features you will use day-to-day. You can always get back to the home page, by clicking “Home” in the toolbar in the upper right.
In addition the toolbar includes a Profile page which has many “occasional use” feature and a Help page with a link to a glossary and other helpful items.

## Slide 8
2
Login
Join Project
Generate
SSH Keys &
SSL Certs
Notes: You should have already logged in by now. And the tutorial leader should have added you to a project.
** If you can’t log in or aren’t in the project, please raise your hand. **
Now that everyone’s ready, please click the profile page to generate and download your SSH keys.
** Live portion: generate keys **

## Slide 9: On your local machine…
> mv ~/Downloads/id_geni_ssh_rsa ~/.ssh/.
> chmod 600 ~/.ssh/id_geni_ssh_rsa
> ssh-add ~/.ssh/id_geni_ssh_rsa
2
Notes: Download the keys generated by the portal. And configure SSH to use them.
These three commands:
* Move the private key generated by the portal into a standard location in the .ssh directory of the user’s home directory
* Changes the permissions on the file so it can’t be read by others
* Adds the ssh private key to your ssh agent.
** Live portion **

## Slide 10: Part I continued: Obtain Resources
slice
3.1 Create a slice
3.2 (optional) Renew your slice
3.3 Reserve two VMs at one aggregate
3.4 Check Whether VMs are Ready to be Used
Layer 2
VM
VM
Notes: First, we will create a slice.
Second, we will optionally renew the slice.
Third, we will reserve resources at two aggregates. There is real work happening here as the nodes are reserved.
Fourth, we’ll determine if the virtual machines have booted and are ready for use.

## Slide 11
3.1
Create Slice
Notes: Now that everyone is a member of the project, let’s click on the project page (you may need to reload your home page).
Now we all need to create a slice using the name XXXX.
** Live: create slice **

## Slide 12
3.2
Extend slice expiration
Notes: Next we will renew the slice to extend the initial expiration time for the resources.

## Slide 13
3.3
Launch
tool
Notes: Next we will reserve resources …..
Today we will reserve resources using Flack. So let’s launch that. This may take a minute.

## Slide 14
Launch
Tool
3.3
Notes: Once Flack is loaded you should be able to see your username, slicename and a long list of aggregates.

## Slide 15
Draw two VMs connected by a link
3.3
Notes: Find the aggregate listed on your worksheet.
Click the VM box next to that aggregate and drag it onto the canvas. Repeat.
Now click near one of the VM boxes on the canvas, then click and drag towards the other VM. Release when you reach the other VM. You should now see a line and a box representing a link connecting the two VMs.

## Slide 16
Change names of VMs
3.3
Notes: Now change the name of the VMs by clicking on the “i” in a circle and editing the name in the pop up.
Make one VM “client” and the other “server”.

## Slide 17
3.3
Set IP and mask of interfaces
Notes: Now change the name of the VMs by clicking on the “i” in a circle and editing the name in the pop up.
Make one VM “client” and the other “server”.

## Slide 18
3.3
Reserve resources
Reserve resources
Bind to an Aggregate
Select a Slice
Notes: When your topology looks like this, press the “Submit” button along the bottom.

## Slide 19
Resources are READY!!!
3.4
Notes: After some time the background will turn green indicating that the resources are ready.

## Slide 20: Experiment Workflow
Part I: Design/Setup
Part II: Execute
Part III: Finish
Notes: In Part II we will execute the meat of the experiment….

## Slide 21: Part II: Execute Experiment
4.1 Login to all three nodes
5.1 Test Connectivity
5.2 Explore the Data and Control Planes
6.1 Logout of nodes
Internet
Data Interfaces
Control Interfaces
ssh
Layer 2
Experimenter
server
client
Notes: We have two nodes (“client” and “server”) and they each have two interfaces. The control interface connects to the public internet and is the interface you use to login to your nodes. The data interface is what we use for the experiment: it’s connected to the VLAN.
We will log into our nodes.
Then we will run our experiment ….
When we are done we’ll log out.

## Slide 22
Login
4.1
Notes: Click on the ssh command to login.
Those using ExoGENI, will need to click the “refresh” button (at the bottom near the Submit) button to get the ssh button to show up.

## Slide 23
$ sudo ifconfig
$ ping 192.168.1.11 –c 5 # server data i/f
$ ping 172.17.1.9 –c 5 # server ctrl i/f
$ sudo ifconfig
NodeB/
NodeC
NodeA
5.1
5.1
Notes: log into your two VMs
Next run ifconfig….
STOP and ….

## Slide 24: Worksheet
Slice Name: lab0<your initials>
5.1
NodeA
eth___
eth___
10.1.1.1
___.___.___.___
NodeB
eth___
eth___
10.1.1.2
___.___.___.___
Data i/f
Control i/f
Data i/f
Control i/f
Internet
Control plane switch
Data plane switch
GENI Rack
Notes: … fill in your worksheet. This is really important.
Be careful.
** Live portion **

## Slide 25
$ sudo apt-get install iperf
$ hash
# server data i/f
$ iperf –c 192.168.1.11
…
# server ctrl i/f
$ iperf –c 172.17.2.4
…
$ sudo apt-get install iperf
$ hash
# start an iperf server
$ iperf -s
NodeB
NodeA
5.1
Notes: Ping the server’s data interface. This should succeed. Let us know if this doesn’t work and we’ll help you debug it.
Ping the server’s control interface. This should also succeed.

## Slide 26
5.1
What is the bandwidth of the data link? Why?
What is the bandwidth of the control link? Why?
NodeA
eth___
eth___
10.1.1.1
___.___.___.___
NodeB
eth___
eth___
10.1.1.2
___.___.___.___
Data i/f
Control i/f
Data i/f
Control i/f
Internet
Control plane switch
Data plane switch
GENI Rack
Notes: What is the bandwidth of the data link? Why?
The bandwidth of the data link is about 100 Mbps which is the default.
What is the bandwidth of the control link? Why?
A lot more. Because you get the full available link.

## Slide 27
Demo here
Notes: When you bring down the data interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.
After you bring down the control interface, your ssh session should immediately hang.
Why?
You brought down the interface you were using to log into the node.
After you bring down the control interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.

## Slide 28
5.2
Configure routing
eth___
eth___
Notes: When you bring down the data interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.
After you bring down the control interface, your ssh session should immediately hang.
Why?
You brought down the interface you were using to log into the node.
After you bring down the control interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.

## Slide 29
5.2
Configure a static route
route add -net 192.168.1.0 netmask 255.255.255.0
gw 192.168.1.1 dev eth0
In above command: | 
add | -Indicates that the route is added to routing table.
-net | -Indicates that desination is a network.
192.168.0.1 | -Indicates IP address of destination network.
netmask | -Indicates the subnetmask of destination network.
From: https://www.hscripts.com/tutorials/linux-commands/route.html
sudo sh -c 'echo 1 > /proc/sys/net/ipv4/ip_forward'
Configure IP routing
Notes: When you bring down the data interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.
After you bring down the control interface, your ssh session should immediately hang.
Why?
You brought down the interface you were using to log into the node.
After you bring down the control interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.

## Slide 30
# ping server data i/f
$ ping 192.168.1.11
…
# ping server ctrl i/f
$ ping 172.17.2.4
…
$ exit
# For ExoGENI only do:
$ sudo service neuca stop
# bring down data i/f
$ sudo ifconfig eth12541 down
# bring down ctrl i/f
$ sudo ifconfig eth999 down
NodeB
NodeA
5.3
5.3
Notes: Ping the server’s data interface. This should succeed.
Next bring down the data interface on the server node.
Your pings should start to fail.
Ping the server’s control interface. This should succeed.
Next bring down the control interface on the server node.
Your ssh connection to the server node should immediately hang.
And your pings should start to fail.

## Slide 31
Demo here
Notes: When you bring down the data interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.
After you bring down the control interface, your ssh session should immediately hang.
Why?
You brought down the interface you were using to log into the node.
After you bring down the control interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.

## Slide 32
5.3
When you bring down the data interface, the destination should become unreachable. Why?
NodeA
eth___
eth___
10.1.1.1
___.___.___.___
NodeB
eth___
eth___
10.1.1.2
___.___.___.___
Data i/f
Control i/f
Data i/f
Control i/f
Internet
Control plane switch
Data plane switch
GENI Rack
Notes: When you bring down the data interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.
After you bring down the control interface, your ssh session should immediately hang.
Why?
You brought down the interface you were using to log into the node.
After you bring down the control interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.

## Slide 33
5.3
After you bring down the control interface, the destination becomes unreachable. Why?
NodeA
eth___
eth___
10.1.1.1
___.___.___.___
NodeB
eth___
eth___
10.1.1.2
___.___.___.___
Data i/f
Control i/f
Data i/f
Control i/f
Internet
Control plane switch
Data plane switch
GENI Rack
Notes: When you bring down the data interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.
After you bring down the control interface, your ssh session should immediately hang.
Why?
You brought down the interface you were using to log into the node.
After you bring down the control interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.

## Slide 34
5.3
After you bring down the control interface, your ssh session should immediately hang. Why?
NodeA
eth___
eth___
10.1.1.1
___.___.___.___
NodeB
eth___
eth___
10.1.1.2
___.___.___.___
Data i/f
Control i/f
Data i/f
Control i/f
Internet
Control plane switch
Data plane switch
GENI Rack
Notes: When you bring down the data interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.
After you bring down the control interface, your ssh session should immediately hang.
Why?
You brought down the interface you were using to log into the node.
After you bring down the control interface, the destination should become unreachable.
Why?
The client can no longer reach that interface on the server.

## Slide 35
You are trying to log in to a compute node on GENI using SSH and can’t.
Which are possible explanations?
You entered the wrong password
You didn’t offer the private key that matches the public key
The public key wasn’t loaded onto the node
Permissions on the private key are too permissive
(b), (c), and (d)
Notes: After some time the background will turn green indicating that the resources are ready.

## Slide 36: Experiment Workflow
Part I: Design/Setup
Part II: Execute
Part III: Finish
Notes: The third part of the experiment is when you would normally archive any data and release your resources.

## Slide 37: Finish
Don’t Delete YET!!!
We will clean up later

## Slide 38
Delete Resources
7
Notes: The delete button is on the bottom of Flack (above the Submit button).

## Slide 39: Part III: Finish Experiment
When your experiment is done, you should always release your resources.
  Normally this is when you would archive your data
  Delete your resources at each aggregate
slice
project
aggregate
experimenter
resource
Notes: Be sure to delete your resources.

## Slide 40: Congratulations!
You have…
  Run your first GENI Experiment!
  Exercised your knowledge of GENI terminology
  Used the GENI Portal and Jacks or jFed
Notes: When we started, we promised to do three things.
You’ve run your first GENI experiment.
You’ve hopefully developed a more concrete understanding of GENI terminology.
You have used the GENI portal and Flack

## Slide 41
Welcome
to GENI!

## Slide 42: Backups

## Slide 43
NodeA
eth___
eth___
192.168.1.10
___.___.___.___
NodeB
eth___
eth___
192.168.1.11
___.___.___.___
Data i/f
Control i/f
Data i/f
Control i/f
Internet
Control plane switch
Data plane switch
GENI Rack

## Slide 44
eth___
eth___

## Slide 45
NodeA
eth___
eth___
192.168.1.10
___.___.___.___
eth___
eth___
192.168.1.11
___.___.___.___
NodeB
Control i/f
Control i/f
Internet
Control plane switch
GENI Rack
NodeC
eth___
eth___
192.168.3.12
Data plane switch
192.168.2.12
192.168.2.11
eth___
eth___
192.168.3.10

## Slide 46
NodeA
eth___
eth___
192.168.1.10
___.___.___.___
eth___
eth___
192.168.1.11
___.___.___.___
NodeB
Control i/f
Control i/f
Internet
Control plane switch
GENI Rack
NodeC
eth___
eth___
192.168.3.12
Data plane switch
192.168.2.12
192.168.2.11
eth___
eth___
192.168.3.10

## Slide 47
NodeA
eth___
eth___
192.168.1.10
___.___.___.___
eth___
eth___
192.168.1.11
___.___.___.___
NodeB
Control i/f
Control i/f
Internet
Control plane switch
GENI Rack
NodeC
eth___
eth___
192.168.3.12
Data plane switch
192.168.2.12
192.168.2.11
eth___
eth___
192.168.3.10

## Slide 48
Data plane switch
NodeA
eth___
eth___
192.168.1.10
___.___.___.___
eth___
eth___
192.168.1.11
___.___.___.___
NodeB
Control i/f
Control i/f
Internet
Control plane switch
GENI Rack
NodeC
eth___
eth___
192.168.3.12
192.168.2.12
192.168.2.11
eth___
eth___
192.168.3.10